## Slide 1
Bounded-error integer storage
for Thermo RAW spectra
Direct conversion · native and vendor input paths
13 RAW files · 49.48 GB · 21 October 2026
Notes: Technical research presentation. Experimental archive, not an official mzPeak file. Full report: docs/WRITEUP.md. Background: https://doi.org/10.1021/acs.jproteome.5c00435 and https://hupo-psi.github.io/mzPeak-specification/. No endorsement or format-conformance claim.

## Slide 2
Compact storage, with different reader tradeoffs
Against official default | Native rawr-ms | Thermo reader
Eligible comparisons | 11 / 13 files | 10 / 13 files
Geometric-mean speedup | 4.74× | 1.74×
Aggregate output reduction | 73.14% | 74.43%
Relative sampled tree RSS | 1.72× official | 0.71× official
Bounded-loss output versus exact retained values. Eligible sets differ; failed comparisons are excluded from ratios.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef.

## Slide 3
Benchmark protocol
49.48 GB across 13 files
Selected from 334 files / 548.43 GB using dataset, instrument and size coverage before timing.
Eight CPUs · 64 GiB allocation · warm filesystem cache
Direct RAW input · Zstd level 3 · 600 s conversion timeout
One excluded warmup. Seven repeats for the first three completed cases; three for remaining cases after the user-requested amendment.
A comparison needs every declared repeat, stable signal fingerprints and independent all-point validation.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. Protocol amendment: native-validation/readers-three/protocol-amendment.json. Inventory and input selection: campaign-plan.json.

## Slide 4
Signal storage and metadata
Layer | Representation | Why
m/z | Block-local linear integers | Explicit relative-error budget
Intensity | Log integers; reserved zero | Dynamic range; exact zeros
Signal blocks | ≤16,384 points + Zstd | Independent decoding
Index | Compressed JSON directory | Locate spectra and blocks
Acquisition metadata | Parquet tables | Scan and precursor context
Both input readers feed the same encoder. The archive is experimental; the Python shim provides partial API compatibility.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. Codec implementation: code/fast_raw/src/main.rs. Metadata and ZIP assembly: code/complete_raw.py. Numerical compression prior art: https://pmc.ncbi.nlm.nih.gov/articles/PMC4047472/.

## Slide 5
Quantization bounds
m/z: Δ = 2bεq; b = block minimum
Rounding gives |x̂ − x| ≤ Δ/2 = bεq ≤ xεq, since x ≥ b.
Intensity: h = 2 log(1 + εI)
Log rounding gives x̂/x between 1/(1 + εI) and 1 + εI.
Zero has a separate code and remains exactly zero.
Total limits: 0.01 ppm m/z and 0.1% intensity. Reader error uses a separate margin; every accepted point is independently checked.
Notes: Exact-arithmetic derivations and floating-point qualification: docs/WRITEUP.md, Error bounds from the quantizers. The implementation checks reconstructed values and integer roundtrips; independent vendor validation enforces total bounds.

## Slide 6
Native conversion is faster across eligible files
Chart: Speedup versus official
| HeLa | Fusion | Eclipse | Ascend | HF | Lumos | Velos | HF-X | QE | QE+
Native | 4.1205 | 5.1547 | 5.3806 | 3.9434 | 4.0377 | 4.5325 | 5.8452 | 5.6578 | 4.4636 | 4.3029
Vendor | 1.7739 | 1.1384 | 0.88014 | 1.7889 | 1.7165 | 1.6058 | 2.8488 | 2.0395 | 2.3988 | 2.0696
Ten shared eligible files shown. A 233.65 s vendor metadata stall makes Eclipse slower by the paired geometric-mean metric.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. Chart uses the ten files eligible for all three modes; all eleven native comparisons are in the report. Values are paired per-file geometric means, not ratios of displayed medians.

## Slide 7
Storage reduction remains with the vendor reader
Chart: Output size / official (%)
| HeLa | Fusion | Velos | QE Plus
Official default | 100 | 100 | 100 | 100
Our archive + vendor | 22.2641 | 58.0629 | 24.2409 | 24.6912
Across eligible sets: 73.14% less storage with native input; 74.43% with vendor input. Precision contracts differ.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. Native and vendor archive sizes differ only slightly on these examples. All zeros are retained in the custom archive; official default can omit interior zero runs.

## Slide 8
Native reader memory is a real tradeoff
Chart: Sampled tree RSS (GiB)
| HeLa | Velos | QE Plus
Native | 1.6448 | 2.4742 | 5.2525
Vendor | 0.7402 | 0.48084 | 0.59532
Official | 1.2433 | 1.0364 | 0.88701
Bounded signal blocks do not make the whole RAW reader and metadata pipeline constant-memory.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. RAM is median sampled summed process-tree RSS, sampled every 50 ms. Shared pages can be counted twice; brief peaks can be missed. GNU time max-process RSS is separately reported.

## Slide 9
Measured fidelity on the big Astral
Absolute error | Mean | 99th percentile | Maximum
m/z (ppm) | 0.001859 | ≈0.007684 | 0.009055
Positive intensity (%) | 0.049948 | ≈0.098950 | 0.09999990
1,511,811,155 points checked
162,582,445 zeros preserved exactly
Whole-run intensity drift: −0.00006401%. Worst scan TIC error: 0.08622%. Downstream biological equivalence remains untested.
Notes: Evidence: publication/evidence/astral-fidelity.json and native-validation/astral-fidelity/fidelity.json. Saved native archive checked against every source value from Thermo. Percentiles use bounded histogram intervals, not samples.

## Slide 10
Queries improve after opening; startup does not
Astral workload | Native | Official
XIC warm query | 1.068 s | 1.234 s
XIC open + first query | 5.195 s | 3.243 s
MS2 warm query | 4.556 s | 7.053 s
MS2 open + first query | 8.693 s | 8.999 s
Warm MS2: 1.55× faster; 3.87 versus 4.75 GiB peak process RSS.
Opening: approximately 4.12 s native versus 1.84 s official. Two workloads; no general SQL performance claim.
Notes: Evidence: native-validation/astral-queries/query-open.json. Seven randomized fresh-process repeats; one native and Arrow worker; warm filesystem; no persistent index or signal cache. XIC: 494 scans, RT20–25 min, m/z524.3 ±5ppm. MS2 batch:50,208 spectra in the same RT window. Selected values independently validated.

## Slide 11
Failures stay in the evidence
Case | Observed result | Comparison
Astral30 | Custom signal encoded; all modes failed metadata | No complete-archive ratio
Exploris vendor | Retained output validated; third repeat timed out | Vendor ratio excluded
Big Astral | Native validated; vendor and official warmups timed out | Native-only timing
Big Astral native median: 268.10 s on the primary node. The earlier 98.63 s diagnostic is not pooled into campaign measurements.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. Failure logs: 10-PXD063416/vendor-3.log; 11-PXD046453/*-0.log;12-PXD049028/*-0.log. A retained valid output does not qualify a mode when a required repeat fails.

## Slide 12
What this experiment establishes
Compact storage with explicit error bounds
A fast native conversion path and a vendor-backed alternative
with a smaller speed advantage.
Before a broader release
Resolve instrument metadata coverage and stalls. Reduce native
reader memory and eager index parsing. Test downstream
identification and quantification.
Research software: preserve original RAW files. Custom signal storage is not official mzPeak format compatibility.
Notes: Primary evidence: native-validation/readers-three/*.json and summary.json. Derived public table: publication/evidence/conversion-results.json. Conversion baseline: HUPO-PSI/mzPeak commit 40c65521dcfdc3d1df22c16f1ef18e6013fc6ef6. rawr-ms: 2a0422f6a407aa66bb8146f636a5451eae0966ef. Full limitations and references: docs/WRITEUP.md. The archive is not official mzPeak; no universal reader, SQL, peptide identification or downstream quantification equivalence claim.